## Slide 1: Strike Line Characterization from IR Images at W7-X
F. Pisano, B. Cannas, A. Fanni, G. Sias, Y. Gao, M. Jakubowski, H. Niemann, A. Puig Sitjes and W7-X Team
﻿EUROfusion Meeting on
Image Processing and Artificial Intelligence
February 25-26, 2020
Greifswald, Germany

## Slide 2: Wendelstein 7-X Stellarator
OP1.2 (2017-2018) (T.S. Pedersen et al., EPS 2018):
Inertially cooled test divertor
High performance discharge 150MJ: 30s @ 5MW
100s plasmas (2MW): 200 MJ
lower divertor targets
contour of confinement region
upper divertor
targets
Optimized stellarator:
5-fold simmetry, 3D shape
Heating power:
10 MW ECRH (30min), 10MW NBI (10s)
10 divertors: 5 lower, 5 upper

## Slide 3: Wendelstein 7-X Stellarator
OP2 (> 2021):
High Heat Flux (HHF) water-cooled divertor
Steady state operation: 30 min
lower divertor targets
contour of confinement region
upper divertor
targets
Optimized stellarator:
5-fold simmetry, 3D shape
Heating power:
10 MW ECRH (30min), 10MW NBI (10s)
10 divertors: 5 lower, 5 upper

## Slide 4: Divertor Strike-Lines
vertical target
low-iota target
central low-loaded target
high-iota target
Courtesy of M. Krause
M. Jakubowski et al. (2018), Rev. Sci. Instr. 89, 10E116
10 IR thermographic systems monitor surface temperature on the 10 divertors
Investigation on heat and particle fluxes, local effects of leading edges and error fields
Regions of highest thermal load  strike lines
A complex interplay of component shape, magnetic field structure, cross- and parallel field transport results in the strike lines observed.

## Slide 5: IR System

## Slide 6: Heat-Flux Image
Vertical Target
Low Iota Target
Middle Target
High Iota Target
1296x324
Horizontal Target

## Slide 7: Strike-Line Segmentation
Strike-line
Hot spots
Leading edges
...
Other thermal events
It is important to segment the image,
i.e. isolate the thermal events with respect to image background and noise,
in order to automatically:
- analyse separately the properties of each single thermal event
- implement the proper control strategies in case of dangerous events

## Slide 8: Strike-Line Segmentation
Strike-line
Hot spots
Leading edges
...
Other thermal events
It is important to segment the image,
i.e. isolate the thermal events with respect to image background and noise,
in order to automatically:
- analyse separately the properties of each single thermal event
- implement the proper control strategies in case of dangerous events

## Slide 9: Strike-line Segmentation
As a first attempt of isolating the strike-line and remove the effect of noise, hot spots and leading edges, a spatiotemporal prefiltering is applied to the video.
Gaussian spatial filter
size 31x31, σ ≈ 15mm
moving average
time filter, w = 0.03s
*
Prefiltering helps avoiding fragmentation

## Slide 10: Strike-line Segmentation
For each profile (each vertical line) of the horizontal and vertical divertor target, the strike-line width is estimated, using the formula for the wetted area*, as
Qprofile line integrated heat-flux along the profile [MW/m]
qmax maximum heat-flux in the profile [MW/m2]
The segmentation is equivalent to consider an
equivalent rectangular profile having:
- heat-flux equal to qmax
- line integrated heat-flux equal to Qprofile
w
profile width
qmax
*M. Jakubowski et al., IAEA FEC 2018
Red area =
Blu area

## Slide 11: Strike-line Segmentation
For each profile (each vertical line) of the horizontal and vertical divertor target, the strike-line width is estimated, using the formula for the wetted area*, as
Qprofile line integrated heat-flux along the profile [MW/m]
qmax maximum heat-flux in the profile [MW/m2]
The asymmetry with respect to the peak position
is estimated on the basis of the ratio between the
line integrated heat-fluxes at both sides of the profile.
*M. Jakubowski et al., IAEA FEC 2018
wL
profile width
qmax
wR
Red area (L/R) =
Blu area (L/R)

## Slide 12: Strike-line Segmentation
For each profile (each vertical line) of the horizontal and vertical divertor target, the strike-line width is estimated, using the formula for the wetted area*, as
Qprofile line integrated heat-flux along the profile [MW/m]
qmax maximum heat-flux in the profile [MW/m2]
Applicable only in the case of a single strike-line
for each target!
*Only heat-fluxes greater than 0.15MW/m2 are
taken into account.
*M. Jakubowski et al., IAEA FEC 2018
wL
profile width
qmax
wR
Red area (L/R) =
Blu area (L/R)

## Slide 13: Strike-line Segmentation
example of strike-line segmentation for standard configuration
3 main objects

## Slide 14: Strike-Line Segmentation

## Slide 15: Strike-Line Characterization
For each object a set of features is calculated
SPATIAL
Area
Perimeter
Centroid Position
Orientation
etc.
THERMAL
Maximum heat-flux
Minimum heat-flux
Mean heat-flux
Median heat-flux
etc.

## Slide 16: Strike Line Characterization

## Slide 17: Strike Line Characterization

## Slide 18: Thanks for Your Attention!
Questions?

## Slide 19: Case Study
Experiment | Comments
20180816.010 | Ref. discharge: standard magnetic configuration, PECRH= 3 MW, ne = 3.5∙1019 m-2
20180816.011 | at 6s, ICC starts ramping up with slope 150A/s in all control coils
20180816.012 | at 6s, ICC starts ramping down with slope -150A/s in all control coils
20180816.014 | at 6s, ICC starts ramping down (up) with slope -150A/s (150A/s) in lower (upper) divertor control coils
20180816.015 | at 6s, ICC starts ramping up (down) with slope 150A/s (-150A/s) in lower (upper) divertor control coils
20180816.016 | at 10s, ICC starts oscillating @5Hz, by gradually increasing the oscillation amplitude to 600A within 5s. Currents in the lower divertors are in antiphase with respect to the currents in the upper divertors.
Strike line control experiments in standard configuration (OP1.2b, XP: 20180816.#)

## Slide 20: Case Study
Strike line control experiments in standard configuration (OP1.2b, XP: 20180816.#)
Ramp
up
Ramp
up
Ramp
down
Ramp
down
AC
Ref
Ramp
up
Ramp
down
Ramp
down
Ramp
up
AC
Ref
010 011 012 014 015 016

## Slide 21: Case Study
Strike line control experiments in standard configuration (OP1.2b, XP: 20180816.#)
016
AC
AC