## Slide 1: Strategy for developing a new synchrotron radiation synthetic diagnostics for the JOREK code
C.Sommariva, M. Hoppe, S. Silburn, E. Nardon and J.P. Graves

## Slide 2: Outline of the presentation
Introduction
3D synchrotron radiation synthetic diagnostic strategy: synchrotron radiation model
3D synchrotron radiation synthetic diagnostic strategy: numerical scheme
Conclusions

## Slide 3
INTRODUCTION

## Slide 4: Disruptions & Runaway electrons
1) disrupting plasma
2) triggering
MMI
3) Plasma cooling:
-MHD instabilities
5) Current Quench (CQ):
-Loss of plasma current (Ip)
→ Toroidal E-field:
6) Runaway Electron beam:
-MeV energy electron beam
-NOT ALWAYS PRESENT
4) Thermal Quench (TQ)
-Loss of confinement
IRE
Ip
T
RE strikes on JET tiles [1-2]

## Slide 5: Introduction
Highly directional synchrotron radiation emitted by RE beams can be observed in both visible and IR spectra
In JET two cameras are capable of observing the synchrotron light emitted by RE beams [3]:
  KLDT-E5WE: fast camera on the visible spectrum (monochromatic)
  KLDT-E5WC: wide angle camera on the IR spectrum (λ=3-3.5μm)
SPI
KL8
KLDT
Vertical
polarimetry
JET SPI,
Fast Visible Cameras,
Vertical polarimetry [3-4]
During the JET RE experiments, videos from KLDTs cameras showed multiple features appearing in the beam radiation patterns:
similar features are simulated using JOREK-RE fluid [5] and the experimental image might be reproduced using the JOREK-particles module
Ip
RE
m=6 islands
m=5 islands
m=4 islands
partial collapse

## Slide 6
3D SYNCHROTRON RADIATION SYNTHETIC DIAGNOSTIC STRATEGY: SYNCHROTRON RADIATION MODEL

## Slide 7: Detected power from plasma EM-radiation
The radiated power detected by a point on the sensor for unit of wavelength , unit of view angle and of surface is described by [6]:
Where:
is and arbitrary direction of the pixel view angle
position on the sensor
orientation of the sensor at the position
distance between a point in space and the pixel position
spectral and full angular distribution of the synchrotron power of an electron emitted towards a pixel
is the electron distribution function
is the speed of light.

## Slide 8: Synchrotron power emitted by test electrons (1)
A test electron distribution can be written as:
Substituting it in the detected power equation and performing the integration in :
Having defined: , and
Calling the view range of the sensor at the position and integrating over :

## Slide 9: Synchrotron power emitted by test electrons (2)
The synchrotron power received by a detector due to a test electron population is obtained integrating over and :
Where:
is the solid angle within which the synchrotron emission is received
are respectively an electron relativistic factor and its pitch angle
The synchrotron radiation wetted region, required for integrating over , is found to be conical with an apex angle of [6-8]:
  Assumption: all synchrotron radiation emitted by a test electron is strictly contained in a cone with an apex angle of

## Slide 10: Full spectral and angular power distribution
The full spectral and angular power distribution of the synchrotron radiation corrected for the finite speed of light is [7-10]:
With: , , : local curvature of the particle orbit
Ultra-relativistic electrons:
Small orbital angles (spherical angles centered on the emission cone):,
The plasma is optically thin (no-interactions between radiation and plasma)

## Slide 11
3D SYNCHROTRON RADIATION SYNTHETIC DIAGNOSTIC STRATEGY: NUMERICAL SCHEME

## Slide 12: JET Camera characteristics and modeling
The characteristics of the JET KLDT-E5WE and KLDT-E5WC cameras are [11]:
Pinhole cameras with an entrance aperture diameter of 3mm
Different pinholes for the top and the bottom of an image:
  Upper image pupil at: -0.324m
  Bottom image pupil at: -0.236m
upper plane
pixel
lower plane
JET KLDT-E5WE/C cameras can be modeled as two point-like observers having visual ranges of and of looking through different detection planes
Each plane is discretised in equally spaced pixels

## Slide 13: Angular integration of the radiated power
pixel
Integration node
light path
LoS
The full synchrotron power distribution has to be integrated over the solid angle :
Write the integral in terms of area integrals
Discretise the surface integral over a pixel with a 2D numerical integration scheme
For each jth - node:
  Compute the node position in terms of orbital coordinates
  Compute the contribution
Compute the surface integral over the pixel area

## Slide 14: Spectral integration
Cameras are sensitive within specific wavelength ranges:
JET KLDT-E5WC: 3 < λ < 3.5μm
JET KLDT-E5WE: ~400 < λ < ~ 700nm
The synchrotron power distribution has to be integrated w.r.t the wavelength for all camera sensitivity intervals.
Spectral integration of the radiated power distribution [11]:
Issue: the modified Bessel functions and are not necessarily supported by mathematical libraries (e.g. CUDA [12]):
Numerical implementations exist but with which performance [13]?
Possible solutions:
Precompute the values of and off-line, store them in a look-up table and interpolate the desired values
Precompute the values of and off-line and train an interpolator using machine learning technique
Standard numerical methods can be used for integrating in after knowing

## Slide 15: Select active electrons for reducing algorithm cost
    Check if the path does not intersect the tokamak boundary
    Check if contained in the electron emission cone
visible paths
blocked paths
pixel
pixel
pupil
Tokamak boundary
For a simulation of 106 particles with a camera defined by 1024 pixels 1.024·109 3D integrations are required: expensive!
  Compute the electron - pixel node radiation paths
  For each radiation path:
Accept path if {A,B,C} are verified
  Check if contained in the pupil visual range
Select only active particles:
For each pixel and for each electron:

## Slide 16: Algorithm overview and parallelisation
The overall algorithm can be split in two different kernels:
find active radiation paths for each pixel:
  Compute the radiation paths of e-
  Check if radiation paths are active
  If a e- has at least one active radiation path, store it as active particle
Compute the radiated power of the jth-e- on the ith-pixel:
  Integrate the radiated power over all -intervals for each integration node
  Integrate the power of each -interval over the pixel surface
Possible time integration over multiple time-slices during a shutter opening period
The parallelisation of the algorithm on a hybrid MPI-GPU architecture is almost perfect:
Pixels are completely independent
e- contributions are almost independent
  a reduction per pixel is required
Proposed strategy:
Split the detector in multiple subdomain
Allocate each subdomain-pupil group to a different MPI communicator
Subdivide the particle group in multiple MPI tasks within each MPI communicator
A task particle list is divided within all GPUs composing a node:
  Reduction operations in communicator
  Time integration based on asynchronous GPU kernels (if implemented)

## Slide 17
CONCLUSIONS

## Slide 18: Conclusions
The power received by a pixel can be modeled as the sum over all particles of the area-spectral integrals of an e- full spectral and angular synchrotron power distribution
    code speed-up may be achieved using simplified models
Spectral integration requires a fast method for evaluating and functions
Solid angle integrals can be performed computing the synchrotron radiation power deposited on the surface of a pixel
Reduction of the computational complexity can be achieved selecting only “active” light paths for each pixel:
  Active paths: paths contained in both the pupil view range and synchrotron emission cone without intersecting the tokamak boundary
A hybrid MPI-GPU strategy can be used for parallelizing the synthetic diagnostic in both pixel-pupil domain and particle list
  Possible use of asynchronous kernels for time integration (if implemented

## Slide 19: References
[1] C. Reux et al., Nucl. Fusion, vol.55, p.093913, 2015
[2] A. Fil, PhD thesis, IRFM, 2015
[3] S. Silburn, JET refresher course, CCFE, UK, 2018
[4] https://users.euro-fusion.org/openwiki/index.php/KL8
[5] V. Bandaru et al., Plasma Phys. Control. Fusion, 2020 (accepted), 10.1088/1361-6587/abdbcf
[6] M. Hoppe et al., Nucl. Fusion, vol. 58, p. 026032, 2018
[7] J. Schwinger, Phys. Rev., vol. 75, p. 1912, 1949
[8] G. R. Blumenthal et al., Rev. Mod. Phys., vol. 42, p. 237, 1970
[9] L. Carbajal et al, Plasma Phys. Control. Fusion, vol. 59, p. 124001, 2017
[10] V. L. Ginzburg et al., Sov. Phys. Usp., vol. 11, p. 34, 1968
[11] S. Silbrun, private communication, 2021
[12] M. Abramowitz, I. A. Stegun, Handbook Mathematical Functions, 1964
[13] CUDA Math API, CUDA Toolkit v11.2.1 Documentation, 2021
[14] Y.C. Keluskar et al., ITM Web Conf., vol. 32, p. 03052, 2020

## Slide 20
BACKUP SLIDES

## Slide 21: The modified Bessel and the Airy functions
Airy’ functions [1]:
Relation between the Airy and the modified Bessel functions [1]:
[1] M. Abramowitz, I. A. Stegun, Handbook Mathematical Functions, 1964

## Slide 22: The useful integrals
Where:

## Slide 23: The useful integrals
Integrals:

## Slide 24: Relations
Frequency and wavelength in vacuum: with the speed of light
Jacobian of the wavelength:
Instantaneous radius of curvature: with : curvature
Instantaneous angular velocity ultra-relativistic limit:
Solid angle: expressed as units of area over the unit of sphere surrounding the apex
  an object which blocks all rays from an apex has a number of steradians equal to the total surface of the unit sphere:
Normalisation used in [1] for the electric field of a charge:
All this trickeries are required for obtaining Eq. 4 of [2] from Eq. II.31 of [1]

## Slide 25: Relations
Solid angle differential: with the surface element, relative position between particle and detector and n the detector orientation dA detector surface area

## Slide 26: Corrections due to doppler effect
Correction to the angular velocity due to Doppler effect:
with : pitch angle and : angle between the direction of the magnetic field and the line-of-sight

## Slide 27: The modified Bessel and the Airy functions
Integrating over all possible view direction :
The distribution function of test particles can be written as:
Hence:

## Slide 28: The modified Bessel and the Airy functions
Integrating over the pixel surface and noting that :
Or in terms of the spherical coordinates and of the particle relativistic factor and pitch angle :